## Slide 1: Useless Lockbox
Daniel Diaz
Dwayne Hoeck
Ha Tran
Thanh Le
Team 09

## Slide 2: Need and Motivation
Need:
  Privacy and security have become major concerns in society today. Whether it be a teenager trying to keep a diary hidden or an adult keeping money away from a less than trustworthy roommate, a lockbox is a good way to go.
  Unfortunately, lockboxes are obvious and sometimes bring with them curiosity as to what is inside. An interesting and elegant way to keep a lockbox without arousing much suspicion is needed.
Motivation
  Privacy
  Entertaining
  Not identifiable as lockbox at first glance
  Environmentally friendly
  Aesthetically pleasing

## Slide 3: Objective
The overall objective of this project is designing and prototyping an elegant lockbox. The locking feature should not be the most distinguishing feature yet still be a secured box of storing items.
Design
  PCB
  Unlock program
  Box
Prototype
  Hardware box
Test
  Input correct code/unlocks/disable
  Input incorrect code/disable

## Slide 4: Alternatives
Conventional lock box
Conventional useless box

## Slide 5: Requirements

## Slide 6: Approach
Useless machine feature incorporation: Simple box with a switch and a moving arm. When the switch is flipped, the arm moves and flips the switch back to the starting position.
Lock box feature: The switch will enable a keypad. If the correct passcode is entered a solenoid will activate and the “hidden” lockbox compartment will open. If the passcode is incorrect a moving arm will flip the switch back to the off position.

## Slide 7: Approach
Split hardware and software
ATmega328P microprocessor interactions:
  LCD
  Keypad
  Servo
  Solenoid
  Switch
Hardware
  Box/Door
  PCB

## Slide 8: Project Schedule

## Slide 9: Design Process
Atmega328P IDE:
  Visual studio + AVR Dragon
Software coding:
  LCD: 4 bits interactions
  Servo: 16bits counter and interrupt service to produce PWM
  Keypad: matrix keypad
Hardware:
  PCB: Eagle and Oshpark
  Box: SOLIDWORK and Laser cutter in L.I.D

## Slide 10: Design Process– Block Diagram

## Slide 11: Design Alternatives and Decision Making
Design alternative
  Visual studio vs Arduino IDE
  4-bit vs 8-bit interaction for LCD
  Interrupt vs pull-up GPIO for keypad
  SOLIDWORKS vs Adobe Reader for box design
  3D-printing vs Laser-cutter for box prototype
Decisions made
  Visual studio:
    Available in lab
    Debugging ability
  4-bit interaction for LCD:
    I/O pins saving
  Interrupt GPIO for Keypad:
    Common pin usage with ISP pins
  SOLIDWORKS: More flexible
  Laser-cutter:
    Faster
    Easy to fix

## Slide 12: Implementation
Major components:
Microprocessor: ATmega328P
Locking Mechanism:
  Key Pad
  16x2 LCD Display
  Solenoid
Useless Box Mechanism:
  Switch
  Servo

## Slide 13: Implementation Coding

## Slide 14: Implementation Pseudo code
While switch on
Ask for 4-key number code
If the code is the pass code: open the box, flip the switch
Else If the code is the reset code: run the reset sequence
Else if the code is admin code: run the change sequence
Else flip the switch

## Slide 15: Implementation - Schematic

## Slide 16: Implementation - Board Layout and Box Model

## Slide 17: Implementation Billing of Materials

## Slide 18: IP and Prior Work
Useless box: Originally designed in 1930s by Italian artist Bruno Munari. The most famous useless box began in 1952 at Bell Labs by Marvin Minsky.
Lock box: The first key lockbox was invented over 55 years ago by Delbert Williams.

## Slide 19: Testing plan
Individual modules testing: servo, keypad, LCD, switch
Integrations test: Correct code/ Admin code/ Incorrect code enter
Acceptance test: does it meet the condition is PDS
  Privacy
  Entertaining
  Environmentally friendly
  Authenticity
  Economic
  Operational physical environments

## Slide 20: Result
A lock box and four working PCBs

## Slide 21: Contribution and Lessons Learning
Contribution: All members are involved in the whole design process.
  Box printing
  Schematic/PCB
  Coding
  Testing
  Writing
Lessons learning: Each team member learns more on working in team.
  Brainstorming process
  Designing
  Decision making
  Issues troubleshooting
  Documentation
  Communication

## Slide 22: Thank you